## Slide 1: Measurement of the Directional Characteristics of Antennas in the Testbed
Master Thesis
19 Jan 2023
By :
Chirag Patel

## Slide 2: Connection flowchart
List of Hardware devices:
MXG Signal Generator
EXA Signal Analyser
Arcus stepper motor
List of software and API:
MatLab
Control Tool box (API)
GUI_CMD.exe
VISA protocol

## Slide 3
MatLab
.mlapp
Application
Connect All
3 Devices
Get full access for control
Choose the Range and Resolution with suggested Pause
Generate a live
Polar plot
Observe the
Data points
Save Data
Compare diff. data sets

## Slide 4
Communication time
Between MXG & EXA
0.1 sec Pause

## Slide 5: Full rotation Time in seconds for the Motor
Total_Time = ( ( Micro_steps / HSPD ) x ∆ Gear_size ) + setteling_Time(sec)
Required time for 1° step Size = Total_Time / 360°
Total_Time = ( ( 3200 / 1000 ) x 5 ) + 20
Total_Time = 16 + 20 = 36 (Sec)
Required time for 1° step Size = 36 / 360° = 0.1 Sec
Example :

## Slide 6
Thank you